## Slide 1
Manikya Lal Verma Textile & Eng. College
Submitted To
Mrs. Hareeta Malani
(Project Guide, Asst. ECE Department)
Submitted By
Ashish Sahu
Shubham Sharma
Vishal Yadav
Dharmendra Saini
Santosh Yadav
Q.G. - 11

## Slide 2: IoT And GSM Based Smart Security System

## Slide 3
Introduction
Introduction of Project
Contribution of Individuals
PCB Layouts
Overall View
Describe by Vishal Yadav
Hardware and component placement
Brief description
Describe by Shubham sharma and Dharmendra Saini
Embedded Coding
Brief Description
Described by Ashish Sahu
MATLAB and IOT Interface
Brief Description
Described by Ashish Sahu

## Slide 4: Aim of Our Project
The aim of our project is to provide privacy and security to a particular Home or companies from remote locations from a central Server system.
the system allows the home owner or company owner to monitor and control the house security like Whose entered, Door lock or door unlocked, which can be switched on or o via the mobile phone set by sending commands in the form of SMS and also the home owner can receive the appliances status.

## Slide 5: Block Diagram

## Slide 6
User Enter

## Slide 7
First
PCB Layout
Implemented By Vishal Yadav
Second
Hardware and component placement
Implemented By Ashish kumar
Third
MATLAB and IOT Interface
Implemented By Santosh Yadav
Fourth
Implemented By ashish,shubham,dhremandra.
Embedded Coding

## Slide 8: PCB Layouts
First Development Board
Second Development Board
Remote and Noise detection Unit

## Slide 9: INTERFACING WITH HARDWARE COMPONENT
USE OF HARDWARE COMPONENT.
USE OUSE OF LCD COMPONENT.
F ESP8266 MODULE.
USE OF FINGURE PRINT SENSOR.
USE OF GSM MODULE.
USE OF PROXIMITY SENSOR.
USE OF SOUND MODULE

## Slide 10: USE OF LCD 16X2

## Slide 11: FINGURE PRINT SENSOR

## Slide 12
First Development Board Circuit Diagram

## Slide 13
PCB Layout of Transmitter Section

## Slide 14
PCB Layout of Atmega 8 Section

## Slide 15: Coding of embedded c

## Slide 16: USING OF IOT BY ESP 8266 MODUE
It is used for send the message signal.
It use for sending the data by using sever.
It can also be easily configured as a web server.
It is a wifi module .
These module accepts commands via a simple serial interface.

## Slide 17: Motion Detector or Theft Detection Unit
The motion sensor gives digital output which has been used as microcontrollers input. When motion has been detected, motion detector gives logical one to the microcontroller.
As a motion sensor we used PIR sensor which allow you to sense motion, almost always used to detect whether a human has moved in or out of the sensor’s range.
They are often referred to as PIR, ”Passive Infrared”, ”Piezoelectric”, or ”IR motion” sensors.

## Slide 18
Algorithm
STEP 1 : START
STEP 2 : FOR each user
STEP 3 : INPUT Action
STEP 4 : SWITCH Action
STEP 5 : CASE “fingerprint”
STEP 6 : IF fingerprint does not match THEN take and send image
STEP 7 : ELSE IF fingerprint is valid THEN open the door
STEP 8 : ELSE IF number of mismatch greater then 3 THEN take and send image
STEP 9 : ELSE go to STEP 2
STEP 10 : CASE “impact”
STEP 11 : Impact Sensor operation
STEP 12 : IF impact value greater then threshold valu THEN camera sensor operation
STEP 13 : ELSE go to STEP 2
STEP 14 : CASE “proximity”
STEP 15 : IF distance greater then threshold value THEN mobile device synchronization
STEP 16 : IF valid user THEN open the door
STEP 17 : ELSE go to STEP 2
STEP 18 : ELSE go to STEP 2
STEP 19 : END

## Slide 19
Simulation

## Slide 20
Coding Section

## Slide 21
Coding Section for User

## Slide 22
Hardware of Theft Detection Unit

## Slide 23: Result
Figure shows the screenshot of the message for the theft detector operation. The user can query all records of comings and goings from the ` Log (Access Record)' menu.

## Slide 24: Fingerprint Verification Unit
This unit monitors real time fingerprint verification data from doors. This unit has its setting limitted tryels.
Above this value, the microcontroller sends message to the users mobile phone that the someone tryed to acces door and crossed its limited trial.
We have used RS305 as fingerprint sensor.

## Slide 25
Simulator

## Slide 26
Coding Screenshots of Fingerprint Section
Function for LCD command

## Slide 27
Display message fro LCD
Message for User for enroll

## Slide 28: Load and Wireless Unit
Protection of home main door is the important part in security system which done in this system by using electromagnetic lock in conjunction with fingerprint module.
The owner using this biometric for valid user which is display on LCD and if the fingerprint matched is correct then the electromagnetic lock is opened. Otherwise if does not matched, the door will still locked.

## Slide 30: Conclusion
The GSM and IOT based advance security system has been designed and tested with the mobile network.
The user can get alerts anywhere through the GSM technology thus making the system location independent.
The web camera based security system is very easy, user friendly and software has many features.
By installing the web camera at the door site, intruder can be detected and owner can receive a message telling the intruder entry in a home.

## Slide 31
MATLAB INTERFACE
Detection
Footage Recording
Image Capturing

## Slide 32
Detection Of Invalid User
Fingerprint Section
User Verification
Invalid User Found
USB to TTL
MATLAB

## Slide 33
Coding Section of Detection Function

## Slide 34
Image Capturing and Storing Unit
Serial Communication
Image captured and stored
Image capturing function activate

## Slide 35
Coding Section of Image Capturing Function

## Slide 36
Video Recording Unit
After the image captured Video recording section is activate.
Captured video can be stored and can be use for investigation process.

## Slide 37
Coding section of Video Recording Unit

## Slide 38
IoT Section
Invalid User Entered
Known/Unknown
MATLAB Interface
Image and Video Recorded
Notification to Admin Using Blynk
Full Control of Admin

## Slide 39
Coding of IoT Section
Image Captured Using MATLAB
Notification with Blynk App
Known
Unknown
Door Control to Admin
Lock
Unlock

## Slide 40
Coding of IoT Section

## Slide 41: References
Yanbo Zhao , Zhaohui Ye "A low cost GSM/GPRS based wireless home security system" IEEE Transactions on Consumer Electronics ( Volume: 54, Issue: 2 ),2008.
C. Pyo, H. Gang, N. Kim and H. Bang, \Technology trends and prospects of development of IoT (M2M)," OSIA Standards & Technology Review, vol. 26, no. 2, (2013), pp. 8-17.
Y. Ko, \Study of Policies of Major Countries on Internet of Things and Market Forecast," In ternational Commerce and Information Review, vol. 16, no. 5, (2014),pp. 27-47.
D. Seo, H. Ko and Y. Noh, \Design and Implementation of Digital Door Lock by IoT," KIISE Transactions on Computing Practices (KTCP), vol. 21, no. 3, (2015), pp. 215-222.

## Slide 42
Thank You